## Slide 1
REVIEW 2 PRESENTATION
DESIGN, DEVELOPMENT & PROGRESS
CTG-CPM: Self-Healing Networks via Counterfactual Telemetry
Predictive Maintenance Recommendation using Generative AI, Game Theory & Multi-Agent Orchestration
PROJECT TEAM & EQUAL CONTRIBUTIONS
• Sagnik Basu (23MID0042)
Architecture, Game Theory Engine & LLM Diagnostics
• C Sriharsha (23MID0111)
Telemetry Ingestion Engine & Live Host/5G Collectors
• Maitree Singh (23MID0076)
Generative Counterfactual Engine & Web App Dashboard

## Slide 2
02 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
OVERVIEW
Abstract & Core Problem Statement
PROJECT ABSTRACT
Current predictive maintenance (PdM) operates as an opaque 'black box' — predicting failures without explaining why or how to fix them.
CTG-CPM is a closed-loop predictive maintenance recommendation system combining:
1. Time-Series Diffusion Models for counterfactual 'What-If' future telemetry.
2. Graph Neural Networks (GraphSAGE) for topology-aware anomaly detection.
3. Algorithmic Game Theory (VCG, Shapley, Nash) for provable agent coordination.
4. LLM-Powered Diagnostics (Groq GPT-OSS) for step-by-step remediation.
THREE CRITICAL INDUSTRY SHORTCOMINGS
1. Opacity ('Black Box')
Predicts failure timestamps but fails to explain the causal chain, leaving NOC engineers stranded.
2. Manual Bottleneck
Engineers guess remediation scripts manually on live traffic, risking catastrophic cascading outages.
3. OPEX Truck Roll Drain
Companies resort to costly physical hardware replacements because they cannot safely test software fixes.

## Slide 3
03 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
ARCHITECTURE
5-Layer System Architecture & Data Flow
1
LAYER 1: DATA INGESTION
Apache Kafka, gNMI, psutil Live Telemetry & InfluxDB Storage
2
LAYER 2: TOPOLOGY GNN
GraphSAGE Topology Mapper & Anomaly Propagation Predictor
3
LAYER 3: GenAI COUNTERFACTUAL
Time-Series Diffusion Model generating parallel 'What-If' futures
4
LAYER 4: AGENTIC GAME THEORY
Multi-Agent Loop: VCG Auction, Shapley RCA, Nash Equilibrium & SPE Solver
5
LAYER 5: REMEDIATION RECOMMENDATION
Counterfactual projection selection; generates a recommended command (NOT auto-deployed)

## Slide 4
04 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
METHODOLOGY
Detailed 4-Stage Process Pipeline
PHASE 01
STAGE 1: DETECT
GNN maps live topology and detects telemetry anomalies (OSNR drops, thermal spikes).
PHASE 02
STAGE 2: GENERATE
Diffusion model generates N synthetic counterfactual future telemetry streams under candidate interventions.
PHASE 03
STAGE 3: SELECT
Agent 1 diagnoses root cause via Shapley Values; Agent 2 runs SPE Game & VCG auction; Agent 3 selects candidate via counterfactual projection.
PHASE 04
STAGE 4: RECOMMEND (NOT DEPLOYED)
Produces a recommended NETCONF/YANG & PowerShell command. Auto-deployment is disabled in the prototype.

## Slide 5
05 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
ALGORITHMS
Algorithm Choice: Core ML & Generative Stack
ALGORITHM 1: TIME-SERIES DIFFUSION MODEL
Counterfactual Telemetry Generation (Diffusion-TS)
• Method: Denoising score matching on multivariate time-series data.
• Intervention Conditioning: Synthesizes 'What-If' streams conditioned on specific actions (e.g. throttle CPU 15% vs increase cooling).
• Protocol Constraints: Ensures generated data obeys physical network laws (valid OSNR, laser bias, packet loss ratios).
ALGORITHM 2: GRAPHSAGE GRAPH NEURAL NETWORK
Topology-Aware Anomaly Detection
• Spatial-Temporal Learning: Learns node embeddings capturing both inter-device graph topology and time-series metric streams.
• Anomaly Propagation Modeling: Predicts downstream cascade failure risk when an optical node or CPU core degrades.
• Dynamic Graphs: Topology refreshed periodically to keep node embeddings current.

## Slide 6
06 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
GAME THEORY
Algorithmic Game Theory & Multi-Agent Stack
1. VCG Auction Task Allocation
Agents bid capability scores on tasks. VCG mechanism guarantees DSIC (Dominant-Strategy Incentive Compatibility) — truthfulness is optimal.
2. Shapley Value Attribution
Axiomatic feature attribution (Efficiency, Symmetry, Linearity, Null-Player) for fair multi-metric root-cause decomposition (e.g. CPU 50%, Temp 30%).
3. SPE Backward Induction Game
Solves extensive-form investment & bargaining game tree. Proves SPE strategy: (Low Investment, Greedy Proposal, Accept) -> Payoffs (13, 0).
4. Nash Equilibrium Coordination
2-Player normal form matrix solver ensures multi-agent remediation strategies converge to a stable Nash Equilibrium, preventing conflicting actions.

## Slide 7
07 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
LLM ENGINE
LLM-Powered Intelligent Diagnostics (llm_diagnostician.py)
GROQ API INTEGRATION (gpt-oss-20b)
• Role: Transforms low-level telemetry, Shapley weights, and game outcomes into structured JSON diagnostics.
• Outputs Generated:
- Human-Readable Problem Title & Description
- Physical Root Cause Explanation
- Step-by-Step Remediation Plan with impact
- Risk Assessment if Unresolved within 1-4 hrs
- Business Outcomes (Truck roll avoided, fix time)
SAMPLE LLM DIAGNOSTIC OUTPUT (JSON)
{ 'severity': 'High', 'problem_title': 'CPU and Memory Saturation', 'root_cause': 'High CPU workload (50% Shapley) combined with memory pressure', 'risk_if_unresolved': 'Thermal throttling & system crash within 2-4 hours', 'remediation_steps': [ {'step': 1, 'action': 'Identify High CPU Procs'}, {'step': 2, 'action': 'Apply CPU Throttle 85%'}, {'step': 3, 'action': 'Optimize Memory Cache'} ], 'truck_roll_avoided': 'potential (not measured)', 'estimated_fix_time': 'decision compute only (excludes deployment)' }

## Slide 8
08 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
PROGRESS
Actual Working Progress Since Review 1
✓ Fully Built Core Engine
Implemented all Python backend modules: game_engine.py, telemetry_collector.py, counterfactual_engine.py, agentic_remediator.py.
✓ Groq LLM Integration
Created llm_diagnostician.py using openai/gpt-oss-20b model for structured, human-readable problem diagnosis and remediation.
✓ HMW-Inspired Web Dashboard
Developed modern glassmorphism web application (app.py + index.html) with real-time graphs, anomaly injection, and diagnostic panel.
✓ Automated Test Suite
test_prototype.py unit/integration tests covering 5 core modules (Kafka test asserts honest status rather than emulating a broker).

## Slide 9
09 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
EVIDENCE
Code Committed & GitHub Repository Evidence
PUBLIC GITHUB REPOSITORY
• Repository URL:
github.com/sagnikbasutaan2004-source/ CTG-CPM-Self-Healing-Networks
• Total Committed Files: 15 production files
• Total Lines of Code: 3,368+ lines
• Security Compliance: Zero API key leakage; GROQ_API_KEY managed via user environment variable.
EXECUTABLE SYSTEM COMPONENTS
• game_engine.py
Backward Induction SPE, VCG, Shapley, Nash
• telemetry_collector.py
Live psutil host + 5G transceiver metrics
• counterfactual_engine.py
'What-If' time-series future generator
• agentic_remediator.py
3-Agent closed-loop orchestrator
• llm_diagnostician.py
Groq LLM structured diagnosis generator
• app.py & templates/index.html
Flask web app & glassmorphism UI
• main.py
CLI orchestrator (in-process decision compute)

## Slide 10
10 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
JUSTIFICATION
Justification for Design & Algorithmic Choices
WHY TIME-SERIES DIFFUSION VS. GANS?
Diffusion models avoid mode collapse, provide superior sample quality, and support conditional generation on intervention variables.
WHY GNN VS. STANDARD CNNS?
Network topology is inherently non-Euclidean; our GNN (GCN or GraphSAGE, reported per run) models spatial node connectivity and cascading failure propagation.
WHY VCG & NASH THEORY VS. HEURISTIC PROMPTING?
Game theory provides formal guarantees (DSIC truthfulness, stable equilibrium) that heuristic prompting lacks.
WHY GROQ CLOUD LPU VS. LOCAL LLMS?
Groq LPU offers fast LLM inference useful for the diagnostic step; it is additive to (not the whole) end-to-end MTTR.

## Slide 11
11 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
FEASIBILITY
Updated Economic Feasibility & Cost Analysis
POTENTIAL OPEX & HARDWARE COST
• Potential Truck-Roll Reduction: May avoid physical hardware replacement by recommending configuration fixes (potential benefit, not measured).
• Possible Hardware Life Extension: E.g., optical laser bias adjustment might extend transceiver lifespan (not yet validated live).
• No New Sensor Cost: Uses existing telemetry streams (SNMP, gNMI, psutil) without new hardware sensors.
CLOUD API & INFRASTRUCTURE COST
• Lightweight Inference: Distilled diffusion model and optimized GNN aim to keep GPU compute costs low (figure not yet benchmarked).
• ROI: Cost-benefit depends on prevented outages; no dollar savings figure is claimed without live data.
• Production Feasibility: 5-layer architecture uses proven open-source components (Kafka, PyTorch, Flask, psutil).

## Slide 12
12 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
IMPACT
Social & Environmental Considerations
🌱 Potential Carbon Footprint Reduction
Potentially fewer technician truck rolls could reduce fuel use from service vehicles (not yet measured).
🌱 E-Waste Mitigation (potential)
Software-based remediation could extend hardware life cycles, delaying premature e-waste generation.
🌱 Reliability Support (potential)
Fast remediation recommendations could support higher SLA uptime; end-to-end MTTR is not yet claimed.
🌱 Human Operator Support
Transitions NOC engineers from manual alert firefighting toward overseeing recommended remediations.

## Slide 13
13 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
ADAPTATION
Problems Encountered & How Team Adapted
Problem 1: LLM Reasoning Syntax & Think Tags
• Issue: Qwen/Llama models initially included internal thinking tags (<think>...</think>) breaking raw JSON parsing.
• Team Adaptation: Adapted parser regex in llm_diagnostician.py & switched to openai/gpt-oss-20b for clean JSON output.
Problem 2: VCG Computation Complexity
• Issue: Calculating full VCG auction social welfare over arbitrary agents can scale exponentially.
• Team Adaptation: Restricted auction search space to active 3-agent domain & implemented fast combinatorial allocation.
Problem 3: Simulation-Reality Gap
• Issue: Synthetic counterfactual futures might deviate from live host behavior.
• Team Adaptation: Added domain randomization and integrated real psutil telemetry baseline to constrain generation.

## Slide 14
14 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
TEAM ROLES
Equal Individual Contribution Breakdown
33.3% Contribution
Sagnik Basu
Reg No: 23MID0042
• System Architecture & Patent Claim Formulation • Game Theory Engine (game_engine.py: VCG, Shapley, SPE, Nash) • Groq LLM Diagnostics Engine (llm_diagnostician.py) • Git Repository Management & Automated Testing
33.3% Contribution
C Sriharsha
Reg No: 23MID0111
• Telemetry Collector Engine (telemetry_collector.py) • Real-Time psutil Host Metric Ingestion (CPU, RAM, Disk, Processes) • 5G Optical Backhaul Transceiver Anomaly Simulator • CLI Controller & Main Pipeline Integration (main.py)
33.3% Contribution
Maitree Singh
Reg No: 23MID0076
• Generative Counterfactual Engine (counterfactual_engine.py) • Multi-Agent Remediation Orchestration (agentic_remediator.py) • HMW-Style Modern Glassmorphism Web App (templates/index.html) • Flask Server REST APIs & UI Visualizations (app.py)

## Slide 15
15 / 15
CTG-CPM // REVIEW 2: DESIGN, DEVELOPMENT & PROGRESS
CONCLUSION
Summary of Review 2 Achievements & Next Steps
REVIEW 2 ACHIEVEMENTS
✓ Functional Prototype with fast in-process decision compute (< a few ms, excludes LLM/deployment).
✓ 15 Production Files committed to public GitHub repository.
✓ Automated Test Suite (5/5 unit & integration tests).
✓ LLM-Powered Remediation Recommendation Engine via Groq API.
NEXT STEPS (ROADMAP TO FINAL REVIEW)
1. Simu5G / ns-3 Sandbox Deployment: Scale testbed to 100+ optical transceiver nodes.
2. Provisional Patent Application (PPA): Complete filing for 3 novel patent claims.
3. Live Enterprise Pilot: Graduate system autonomy from advisory to semi-autonomous execution.